SECTION 11 30 00

RECESSED DRYER VENT

Display hidden notes to specifier. (Don't know how? Click Here)

** NOTE TO SPECIFIER ** In-O-Vate Technologies, Inc. ; Recessed Dryer Vent Box products.
 .
 This section is based on the products of  In-O-Vate Technologies, Inc. , which is located at:
810 Saturn St. Suite 21 
Jupiter, FL 33477
Toll Free Tel: 888-443-7937
Tel: 561-743-8696
Fax: 561-745-9723
Email: todd@dryerbox.com
Web: www.dryerbox.com

[ Click Here ] for additional information.

The Dryerbox by In-O-Vate Technologies, Inc. provides a UL rated through penetration firestop system receptacle recessed in the wall to house the dryer flex transition hose.  This receptacle allows both the washer and dryer appliances to be moved back an extra 4 inches or more which in turn provides close to two extra square feet of living area and may also solving a wall layout problem.  It is available from over 1,300 wholesale suppliers throughout the United States and will save money and space.
 
 The Dryerbox is a UL classified metal receptacle that installs recessed in the wall behind the clothes dryer.  It safely and efficiently collects the flex transition hose, allowing the dryer to be installed flush against the wall. The new Down-Box™ in now offered for houses built on stem wall or for second floor laundry rooms.

PART 1    GENERAL

1.1	SECTION INCLUDES

** NOTE TO SPECIFIER **  Delete items below not required for project.

A.	Recessed Dryer Box.

B.	Radiused Dryer Exhaust Vent Fitting

C.	Dryer Vent Accessories

1.2	RELATED SECTIONS

** NOTE TO SPECIFIER **  Delete any sections below not relevant to this project; add others as required.

A.	Section 06 10 00 - Rough Carpentry.

B.	Section 05 50 00 - Metal Fabrications.

C.	Section 07 84 13 - Penetration Firestopping Mortars.

D.	Section 09 22 16 - Non-Structural Metal Stud Framing.

E.	Section 09260 - Gypsum Board Assemblies

1.3	REFERENCES

** NOTE TO SPECIFIER **  Delete references from the list below that are not actually required by the text of the edited section.

A.	ANSI/UL 1479 (ASTM E 814) - Standard Method of Fire Tests of Though Penetration Firestops.

1.4	SYSTEM DESCRIPTION

A.	Dryerbox is a UL classified metal receptacle that installs in the wall behind the clothes dryer. It safely and efficiently collects the flex transition hose, allowing the dryer to be installed flush against the wall. Eliminating the bends in the flex exhaust hose provides for better, less restrictive airflow, which in turn minimizes lint buildup, saves energy costs and reduces the serious fire hazard caused by lint buildup.

1.5	SUBMITTALS

A.	Submit under provisions of Section 01 30 00.

B.	Product Data:  Manufacturer's data sheets on each product to be used, including:

1.	Preparation instructions and recommendations.

2.	Storage and handling requirements and recommendations.

3.	Installation methods.

** NOTE TO SPECIFIER **  Samples may be requested for large project requiring multiple devices. Delete for smaller projects.

C.	Verification Samples:  For each finish product specified, two full size samples, representing actual product.

D.	Manufacturer's Certificates: Certify products meet or exceed specified requirements.

1.6	QUALITY ASSURANCE

A.	Manufacturer Qualifications: Manufacturer: Company specializing in manufacturing products specified in this section with minimum three years documented experience.

1.7	DELIVERY, STORAGE, AND HANDLING

A.	Store products in manufacturer's unopened packaging until ready for installation.

B.	Protect materials from exposure to moisture. Do not deliver until after wet work is complete and dry.

C.	Store materials in a dry, warm, ventilated weathertight location.

PART 2    PRODUCTS

2.1	MANUFACTURERS

A.	Acceptable Manufacturer:  In-O-Vate Technologies, Inc. , which is located at: 810 Saturn St. Suite 21 ; Jupiter, FL 33477; Toll Free Tel: 888-443-7937; Tel: 561-743-8696; Fax: 561-745-9723; Email: todd@dryerbox.com; Web: www.dryerbox.com

** NOTE TO SPECIFIER **  Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

B.	Substitutions:  Not permitted.

C.	Requests for substitutions will be considered in accordance with provisions of Section 01 60 00.

2.2	DRYER VENTS

A.	Dryer Vents General:

1.	UL Classified for a 1-hour F-Rating in accordance with ANSI/UL 1479 (ASTM E 814).

2.	Fabricated using a deep drawn aluminum manufacturing process.

3.	Extension rim protrudes from nailing flange 7/8 inch (22 mm).

4.	Fabricated with eight 1/4 inch (6 mm) mounting holes (4 on each side).

5.	Sides are tapered to allow for nesting of multiple boxes.

6.	Provided with surface that is clean of any oil residue and will adhere paint.

7.	Provided with a Gas Port knock-out.

** NOTE TO SPECIFIER **  Select one of the following Dryer vents from the following paragraphs as required for the project. If multiple types are required indicate the location of each on the Drawings. Delete the paragraphs for the products not required.

B.	Model 425: Sku DB-425 for Upward Exhaust Direction.

1.	Fabricated of 22 gauge aluminized steel and weighing 4.14 pounds (1.88 kg) each.

2.	Top port measures 4-1/8 inches (105 mm) with very slight oval shape.

3.	Distance from nailing flange to rear of box is 4-1/4 inches (108 mm).

4.	Overall measurements: 21 inches (533) high by 12-1/2 inches (318 mm) wide by 5-1/8 inches (130 mm) deep.

5.	Inside measurements are 9-1/2 inches (241 mm) wide by 18-1/4 inches (464 mm) tall.

C.	Model 350: Sku DB-350 for Upward Exhaust Direction.

1.	Fabricated of 22 gauge aluminized steel and weighing 4.03 pounds (1.83 kg) each.

2.	Top port measures 4-7/8 inches (129 mm) by 3-1/8 inches (79 mm) oval shape.

3.	Distance from nailing flange to rear of box is 3-1/2 inches (89 mm).

4.	Overall measurements: 21 inches (533 mm) high by 12-1/2 inches (318 mm) wide by 4-3/8 inches (111 mm) deep.

5.	Inside measurements are 9-1/2 inches (241 mm) wide by 18-1/4 inches (464 mm) tall.

D.	Model 4D: Dryerbox for Downward Exhaust Direction.

1.	Fabricated of 22 gauge aluminized steel and weighing 4.31 pounds (1.9 kg) each.

2.	Lower port measures 4-1/8 inches (105 mm) with very slight oval shape.

3.	Distance from nailing flange to rear of box is 4-1/4 inches (108 mm).

4.	Overall measurements: 19 inches (483 mm) high by 16-3/4 inches (425 mm) wide by 5-1/8 inches (130 mm) deep.

5.	Inside measurements are 14 inches (356 mm) wide by 16 inches (406 mm) tall.

E.	Model 3D: Dryerbox for Downward Exhaust Direction.

1.	Fabricated of 22 gauge aluminized steel and weighing 4.12 pounds (1.87 kg)  each.

2.	Lower port measures 4-1/4 inches (107 mm) wide with slight oval shape.

3.	Distance from nailing flange to rear of box is 3-1/2 inches (89 mm).

4.	Overall measurements: 19 inches (483 mm) high by 16-3/4 inches (425 mm) wide by 4-3/8 inches (111 mm) deep.

5.	Inside measurements are 14 inches (356 mm) wide by 16 inches (406 mm) tall.

F.	Retro-Fit Box Model 400: Sku DB-400.

1.	Fabricated of 22 gauge aluminized steel.

2.	Powder coated.

3.	Top port measures 4-7/8 inches (129 mm) by 3-1/8 inches (79 mm) oval shape.

4.	Distance from mounting flange to rear of box is 4 inches (102 mm).

5.	Overall measurements: 21 inches (533 mm) high by 11-1/2 inches (292 mm) wide by 4 inches (102 mm) deep.

6.	Inside measurements are 9-1/2 inches (241 mm) wide by 18-1/4 inches (464 mm) tall.

7.	Two mounting 3/16 inches (4.8 mm) holes on lower flange.

2.3	DRYER VENT ACCESSORIES

A.	Dryer Vents Accessories:

1.	Dryer ducting must be a minimum of 4 inches (102 mm) in diameter.

2.	Provide foil type or aluminum flexible transition hose between the dryer and the wall outlet.  Do not use the plastic or vinyl.

3.	Concealed ducting must be rigid metal (galvanized or aluminum) duct.

4.	Provide exterior rain hood or roof jack at the termination of dryer venting to the exterior.

** NOTE TO SPECIFIER **  Select the following optional exhaust fitting paragraph for use with the Dryer vent specified as required for the project. Delete if not required.

B.	Exhaust Fitting Dryer-ell: Re-engineered metal dryer exhaust fitting fabricated with a larger radius and a smooth interior and providing a net gain of approximately 4.8 feet (1.46 m) in allowable duct length when used as a replacement to the standard 4 inches (102 mm) ell.

PART 3    EXECUTION

3.1	EXAMINATION

A.	Do not begin installation until blocking has been properly prepared.

B.	Verify rated walls are ready for Dryer box installation.

C.	Check location of air outlets and inlets and make necessary adjustments in position to conform to architectural features, equipment arrangement.

D.	Verify surfaces are ready to receive work.

E.	Verify sizes of equipment connections before fabricating transitions.

F.	If preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

3.2	PREPARATION

A.	Wipe exterior surfaces of vent with solvent prior to installation for all surfaces to be painted after installation.

** NOTE TO SPECIFIER **  It is recommended that installation is done as soon as possible to minimize conflict with other construction.

3.3	INSTALLATION

A.	Install in accordance with manufacturer's instructions and the applicable local building code.

B.	For fire rated installations install in accordance with ANSI/UL 1479 (ASTM E 814). Fire rated installations require that voids on the side and above the installation be tightly filled with fiberglass batt or mineral wool batt insulation.

** NOTE TO SPECIFIER **  Select the following paragraph for use with typical installations. Not applicable for stackable or pedestal mounted Dryers. Delete if not applicable.

C.	Install dryer vent as low as possible so that the bottom tab is at or slightly below the finished floor level (not applicable if stackable unit or on a pedestal).

D.	Attach dryer vent to stud and bottom plate at a minimum of 3 corners with drywall screws.

** NOTE TO SPECIFIER **  Select the following paragraph for use with typical installations. Not applicable for stackable or pedestal mounted Dryers. Delete if not applicable.

E.	Install dryer vent with the port up or on its side if necessary.

** NOTE TO SPECIFIER **  Select the following paragraph for use with stackable or pedestal mounted Dryers. For downward exhaust direction use the "Down-Box" Model 4D or 3D. Consult with manufacturer for additional information. Delete if not applicable.

F.	Install Dryer vent with the port down for use with stackable or pedestal mounted Dryers.

** NOTE TO SPECIFIER **  When installing the 4-14 inch deep Dryerbox® (Model 425) into a 2 by 4 inch framed wall, fir out the wall 3/4 inch with a 1 by 2 inch furring strips to provide adequate mounting depth or use the 3-1/2 inch Model 350. Delete if not applicable.

G.	If required fir out the wall framing to provide adequate mounting depth.

** NOTE TO SPECIFIER **  Select the following paragraph for use with exterior wall installations. Delete if not applicable.

H.	When installing in an exterior frame wall, add insulation or duct board to the back side of box to minimize condensation and temperature transfer.

I.	Dryer conduit shall penetrate top port 2 inches (51 mm) to provide for adequate transition hose connection and to properly facilitate its storage recoil.

J.	Duct joints shall be installed with the male end of the duct pointed in the direction of the airflow.

K.	Install Dryer vents with airtight connection.

L.	Secure all joints with metal tape. The use of duct tape is not permitted.

M.	Do not use rivets or screws in the joints or anywhere else in the duct as these will encourage lint collection.

N.	Length of concealed rigid metal ducting shall not exceed 25 feet.  Deduct 5 feet from the allowable length for every 4 inch (102 mm) radius 90 degree elbow and two and a half feet for every 45 degree fitting.  These lengths may vary per local codes and dryer manufacturers recommendations.

O.	Dryer venting shall be independent of any other systems including exhaust vents.

P.	Termination of dryer venting must be to the exterior with a proper hood or roof jack equipped with a backdraft damper.

1.	Small orifice metal screening should not be part of the hood or roof jack as this will catch lint and block the opening in a very short time.

2.	The hood opening should point down and exhibit 12 inches of clearance between the bottom of the hood and the ground or other obstruction.

** NOTE TO SPECIFIER **  Select the following paragraphs as required for project. Delete if not applicable.

Q.	Coordinate work with Section 09 21 16 - Gypsum Board Shaft Wall Assemblies.

R.	Coordinate work with Section 03 63 00 - Epoxy Grouting.

S.	Coordinate work with section 09900 -  Painting to assure that the perimeter of the vent is caulked prior to painting.

3.4	PROTECTION

A.	Protect installed products until completion of project.

B.	Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION